This page was exported from New Lead2pass Dumps PDF Version Released For Free Downloading [    https://www.pass4suredumps.org    ]

Export date: Wed Apr 17 19:41:56 2024 / +0000 GMT

## [January 2018] Lead2pass Free 1Y0-230 Exam Questions Download 100% Pass 1Y0-230 Exam 75q

Lead2pass Free Citrix 1Y0-230 Braindumps VCE Updated:;

https://www.lead2pass.com/1y0-230.html

QUESTION 1

Scenario: A Citrix Administrator entered the command-line interface commands below to prevent IP address 10.10.10.100 from accessing the NetScaler on port 80.

add simpleacl rule1 DENY -srclP 10.10.10.100 -TTL 600

add simpleacl rule2 DENY -srclP 10.10.10.100 -destPort 80

add ns acl rule1 DENY -srclP 10.10.10.100 -priority 10

add ns acl rule2 DENY -srclP 10.10.10.100 -priority 100

apply ns acls

Which Access Control List (ACL) will the NetScaler use to deny the IP address?

A.    add ns acl rule1 DENY -srclP 10.10.10.100 -priority 10

B.    add simpleacl rule1 DENY -srclP 10.10.10.100 -TTL 600

C.    add simpleacl rule2 DENY -srclP 10.10.10.100 -destPort 80

D.    add ns acl rule2 DENY -srclP 10.10.10.100 -priority 100

Answer: B

QUESTION 2

A Citrix Administrator needs to create a customized blacklist of IP addresses to supplement the Webroot reputation check, and in order to have stricter access through NetScaler. How can the administrator create this blacklist?

A.    Create several extended Access Control List policies

B.    Create a data set tor IPv4 address matching.

C.    C. Enable MAC-based Forwarding

D.    Create several simple Access Control List policies.

Answer: A

QUESTION 3

Scenario: A NetScaler has two interlaces as 1/1 and 1/2 with MAC-based Forwarding enabled below are the specifications

- Interlace 1/1 and IP 192 168 10.10 is bound to VLAN 10

- On Interlace 1/2 VLAN 20 and VLAN 30 are tagged

- VLAN 20 is bound to IP 192.168 20 10 and VLAN 30 is bound to 192.168.30 10

The NetScaler receives a packet tor VIP 192 168.30.30 on interface 1/1. Which interlace of NetScaler will send a reply back in this environment?

A.    Interface 1/1

B.    NetScaler will drop the packet received on interface 1/1

C.    Interface 1/2

D.    NetScaler will reply on interfaces 1/1 and 1/2

Answer: C

QUESTION 4

Scenario: A Citrix administrator configured a new NetScater Unified Gateway. The administrator would like to see what Endpoint Analysis and Single Sign-on failures have occurred since implementing the new Gateway.

Which tool can the administrator use to see this data?

A.    NetScater Dashboard

B.    MAS Gateway Insight

C.    aaad.debug

D.    MAS Security Insight

Answer: A

QUESTION 5

Which two options should a Citrix Administrator consider when adding a secondary device in a high availability (HA) pair? (Choose two.)

A.    The Independent Network Configuration (INC) mode should be enabled.

B.    Both the devices should have different SNIP addresses.

C.    The nsroot password should be same on both nodes.

D.    HA Monitoring should be disabled on all the unused interfaces.

E.    Configure the HA status of the Primary Node as STAYPRIMARY.

Answer: AB

QUESTION 6

Scenario: A Citrix Administrator suspects an attack on a load-balancing virtual server. The administrator needs to restrict access to the load-balancing virtual server (192.168.100.25) for 10 minutes.

Which Access Control List (ACL) will help to accomplish this requirement?

A.    add ns acl rule1 DENY -destIP 192.168.100.25 -TTL 600000

B.    add simpleacl rule1 DENY -srcIP 192.168.100.25 -TTL 600

C.    add ns acI rule1 DENY -destIP 192.168.100.25 -TTL 600

D.    add simpleacl rule1 DENY -srcIP 192.168.100.25 -TTL 600000

Answer: C

QUESTION 7

Scenario: A Citrix Administrator has a NetScaler SDX appliance with several instances configured. The administrator needs one instance with two interfaces connected to forward packets that are NOT destined for its MAC address. Hence, the administrator has enabled Layer 2 mode. After enabling Layer 2 mode, the administrator found the interface status going up and down.

What can the administrator perform to resolve this issue?

A.    Disable Layer 2 mode on a NetScaler instance.

B.    Enable MAC-based Forwarding mode.

C.    Enable tagging on all interfaces.

D.    Enable Layer 3 mode along with Layer 2 mode.

Answer: C

QUESTION 8

Which two features can a Citrix Administrator use to allow secure external access to a sensitive company web server that is load-balanced by the NetScaler? (Choose two.)

A.    ICA proxy

B.    Integrated caching

C.    Application Firewall

D.    AppFlow

E.    AAA

Answer: AE

QUESTION 9

Which two components need to be configured for SmartAccess? (Choose two.)

A.    Configuration logging

B.    XenDesktop policies

C.    XML Trust

D.    StoreFront server groups

Answer: CD

QUESTION 10

Scenario: A user is attempting to access a web server, which is load-balanced by the NetScaler using HTTPS. The user received the following message:

SSL/TLS error: You have not chosen to trust "Certificate Authority" the issuer of the server's security certificate.

What can a Citrix Administrator do to prevent users from viewing this message?

A.    Ensure that the intermediate Certificate is linked to the Server Certificate.

B.    Ensure that the user has the Server Certificate installed.

C.    Ensure that the intermediate Certificate is linked to the Root Certificate.

D.    Ensure that the user has the Certificate's Public key.

Answer: C

1Y0-230 dumps full version (PDF&VCE): https://www.lead2pass.com/1y0-230.html

Large amount of free 1Y0-230 exam questions on Google Drive: https://drive.google.com/open?id=0B3Syig5i8gpDajVrZ1J5d3hvQms

Maybe you also need:

1Y0-240 exam dumps: https://drive.google.com/open?id=0B3Syig5i8gpDdmJKZ3FmSnRqa0E

Post date: 2018-01-25 06:23:46

Post date GMT: 2018-01-25 06:23:46

Post modified date: 2018-01-25 06:23:46

Post modified date GMT: 2018-01-25 06:23:46

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com